## Slide 1: Let’s Fix TI, Today
The metric costs us X% on energy accuracy. We can fix it right now with existing hardware.

## Slide 2
10-minute TI is the right answer to the wrong question
We already know how to handle turbulence in a robust way
This can be fixed today, with existing hardware
Notes: Point 2: The same local- and meso-scale physics that drive shear and stability are responsible for turbulence. We already know how to account for this! We just need to finish the job.

## Slide 3
1957 spectral gap image here
Talk about low freq ‘weather’ vs high freq ‘turbulence’
Notes: Low freq weather tells you how windy this afternoon, what the temp will be, will it snow, etc. Most of the useful info is here
High freq tells you how ‘gusty’ the wind is, and thats about it

## Slide 4: Wrong Question:
How can we separate the more predictable, geography-driven ‘weather’ from the less predictable, locally-driven ‘turbulence’?
Right answer:
10 minute averaging and TI metric

## Slide 5
1957 spectral gap image here
Draw red line at 10-min
Notes: low frequency is resolved directly with 10 minute data
High frequency is lumped into one number: TI

## Slide 6
Two main problems with this
Spectral gap is not universal – no neat separation between weather and turbulence. The line is arbitrary. Nothing sacred about 10 minutes.
10 minute frequency is too slow for turbines
Annotated spectral gap here
Notes: A number of studies have tried to replicate the ‘spectral gap’ finding from 1957. Some succeeded, and some failed. Shows that it is not universal. Geographically dependent. Would be great if I could overlay some negative results on top of original 1957 line for a visual. Some sources cited here https://ttu-ir.tdl.org/bitstream/handle/2346/73173/WON-DISSERTATION-2017.pdf?sequence=1

## Slide 7: Look inside a 10-minute data point
Plot a low frequency sine wave
Your met mast describes this 10 minute window as mean X, std Y, TI Z
Maybe also have a ‘minimap’ of where each of these freqs is on the spectral gap image.
Reveal high freq sine wave after discussion
Your met mast describes this 10 minute window as mean X, std Y, TI Z
Your 10-minute data tells you these are identical. If your data says these are identical, then your WRA tells investors that these are identical.
Do you think your turbine thinks they’re identical?
Notes: I’m going to use a very unrealistic fake timeseries here just to clearly illustrate the point, and I’ll follow up later with real world data.
Turbine experiences these very differently. Remember, a turbine is constantly hunting for max power output; it adjusts the pitch of the blades and yaw of the nacelle to match the wind conditions.
In low freq example, the wind changes slowly enough the the turbine can dial in to that wind speed and extract every drop of power
In high freq, the wind is changing so fast that the turbine can’t pitch and yaw to keep up, so power production is much lower. Due to efficiency sensitivity to angle of attack, possible that production is actually lower than the mean [but real amplitudes are much lower, so efficiency is approx. constant. Speed variation ONLY matters if the amplitude takes the speed outside of the AoA tolerance of the blade. May have to apply transform to amplitudes]

## Slide 8: Nice theory, but prove it
Overlay of high, med, low TI power curves
Show that as average TI goes up, power goes up/down depending on where in curve you are. Cite PCWG

## Slide 9: Nice theory, but prove it
Show Prevailing Analysis turbine performance matrix (2014 presentation here "E:\Users\tpbus\Desktop\Transfer\usa\Conference presentations.7z“)
Note that as TI goes up, in ALL conditions (except at rated) power goes UP! Opposite of expected. Shows that there is more energy than expected – low freq variation explains that.